## Slide 1
Peter Atma
MDO Lab University of Michigan
AIAA Aviation, June 13, 2023
Copyright © by Peter Atma, University of Michigan. Published by the American Institute of Aeronautics and Astronautics, Inc., with permission.
Comparing Hydrogen and Jet-A for an N+3 Turbofan with Water Recirculation using Gradient-Based Optimization

## Slide 2: Motivation
Due to climate change, alternative aviation fuels are actively being researched
Hydrogen presents itself as the most viable alternative to kerosene-based fuels

## Slide 3: Motivation
Modern turbofan engines can run off hydrogen with limited modifications
Hydrogen eliminates carbon emissions with water being the main by-product of combustion

## Slide 4: Motivation
Hydrogen-powered engines present a few technological obstacles to being a replacement for Jet-A fuel
Hydrogen tanks need to be stronger and more insulated to keep hydrogen in liquid form, potentially increasing weight
Using water recirculation can potentially offset these negative effects by increasing efficiency and thrust

## Slide 5: Presentation Roadmap
Computational Tools
Water Recovery Model
Propulsion Model
Optimization Problem
Results
Condenser Design Space Sweep
Summary

## Slide 6: Computational Tools
Computational Tools
Water Recovery Model
Propulsion Model
Optimization Problem
Results
Condenser Design Space Sweep
Summary

## Slide 7: OpenMDAO
OpenMDAO is an open-source platform for multidisciplinary design analysis written in Python
Primarily supporting gradient-based optimization, it allows users to explore large design spaces with complex models

## Slide 8: pyCycle
pyCycle is a zero-dimensional engine cycle modeling tool written on top of the OpenMDAO framework
It uses modular components and chemical equilibrium analysis (CEA) solver to converge engine designs to determine performance

## Slide 9: pyOptSparse and SNOPT
The pyOptSparse framework provides a Python interface for nonlinear constrained optimizers
We use SNOPT, a gradient-based sequential quadratic programming (SQP) algorithm for large-scale constrained problems

## Slide 10: Computational Tools
Computational Tools
Water Recovery Model
Propulsion Model
Optimization Problem
Results
Condenser Design Space Sweep
Summary

## Slide 11: Water Recovery Model
An injector component was created in pyCycle
Injects a water flow rate and uses CEA to find the new equilibrium componsition

## Slide 12: Water Recovery Model
Similarly, an extractor component was created in pyCycle
Uses CEA to find the molar fraction of water and extracts a given mass fraction

## Slide 13: Water Recovery Model
The injector and extractor create a feedback loop that creates a mis-match between mass flow rates
We use a nonlinear Newton solver to satisfy conservation of mass

## Slide 14: Computational Tools
Computational Tools
Water Recovery Model
Propulsion Model
Optimization Problem
Results
Condenser Design Space Sweep
Summary

## Slide 15: Engine Model

## Slide 16: Modeling

## Slide 17: Computational Tools
Computational Tools
Water Recovery Model
Propulsion Model
Optimization Problem
Results
Condenser Design Space Sweep
Summary

## Slide 18: Optimization Problem

## Slide 19: Computational Tools
Computational Tools
Water Recovery Model
Propulsion Model
Optimization Problem
Results
Condenser Design Space Sweep
Summary

## Slide 20: Results

## Slide 21: Computational Tools
Computational Tools
Water Recovery Model
Propulsion Model
Optimization Problem
Results
Condenser Design Space Sweep
Summary

## Slide 22: Condenser Design Space Sweep

## Slide 23: Summary

## Slide 24: Backup

## Slide 25
Please note formatting guidelines below.
  Landscape orientation
  16:9 ratio
  Font
    Sans serif (e.g. Helvetica, Arial, Tahoma)
    Sized 24-40 points
  Minimal information—highlight main points
  No commercialism/advertising
  Can your slides be easily read from 15 meters away?
Presentation Title